Metal Ceiling Surfaces Specification Guidelines – CSI Format

Part 1: General

1.01 Related Documents

- Conditions of the Contract and portions of Division One of this Project Manual apply to this section as though repeated herein.

1.02 Work Included

- Metal Ceiling Panels.

- Suspension System for D1 Series Metal Panels

1.03 Related Work

- Ceiling Suspension Systems (D3 Ceiling Panels): Section 09120.

- Mechanical (Air Supply and Return Devices): Division 15.

- Electrical (Light Fixtures): Division 16.

1.04 Submittals

- Submit the following:

  - One full size ceiling panel.

  - One 12 inch long piece of perimeter trim (D1 Series).

  - Manufacturer’s product specifications and installation instructions.

1.05 Delivery, Storage and Handling

- Deliver materials in original, unopened protective packaging, with manufacturer’s labels legible and intact, indicating brand name, pattern and size.

- Store materials in original protective packaging to prevent soiling and physical damage.

1.06 Project Conditions

- Do not install interior acoustical ceilings until space is enclosed and weatherproof.

1.07 Extra Materials

- Deliver extra materials, equal to three percent or more, of each type of metal panel supplied.

- All cartons shall be new and unopened, packaged with protective covering for storage, and identified with appropriate labels.

Part 2: Products

2.01 Manufacturer

- The Gage Corporation International

803 South Black River Street

Sparta, Wisconsin 54656

1-800-786-4243 and 608-269-7447

FAX 608-269-7622

2.02 Profile System D1/M1

- Panel:   (D1.1 flat)   (D1.2 coffer)   (M1.1 flat)   (M1.2 coffer) concealed snap-in ceiling panel.

  - Design:

  - Finish: (Gloss levels from 30 to 100 percent +/- 5%)

  - Size: 24 in. x 24 in. (D1), or 600 mm x 600 mm (M1.1).

  - Metal: 0.030 aluminum (at least 50% recycled).

  - Flame Spread: Class 1, ASTM E84.

  - Optional acoustical perforation with acoustical membrane:

  - NRC: 0.75 flat profile and 0.52 coffered profile perforated panel.

- Carrier: Concealed snap in grid by Gage or equal, 1.5 inch black iron and hanging wire by others.

- Perimeter Trim: ‘C’ channel with hold down clips.

2.03 Profile System D3

- A. Panel:   (D3.1 flush flat)   (D3.2 coffer flat)   (D3.3 flat tegular)   (D3.4 coffer regular)    (D3.5 flat tegular for 9/16” T-grid) lay-in ceiling panel.

  - Design:

  - Finish: (Gloss levels from 30 to 100 percent +/- 5%)

  - Size: 24 in. by 24 in. nominal.

  - Metal: 0.030 aluminum (at least 50% recycled).

  - Flame Spread: Class 1, ASTM E84.

  - Optional acoustical perforation with acoustical membrane: NRC: 0.75 flat profile and 0.52 coffered profile perforated panel.

- Suspension System: Refer to Section 09120

Part 3: Execution

3.01 Examination

- Examine surfaces scheduled to receive suspended units for unevenness, and irregularities that would affect quality and execution of work. Do not proceed with work until unsatisfactory conditions have been corrected.

3.02 Installation

- Do not begin installation until sufficient materials to complete a room are received.

- Install materials in accordance with manufacturer’s printed instructions, governing regulations, fire resistance rating requirements, and industry standards applicable to work.

- Measure each ceiling area and establish layout of acoustical units to balance border widths at opposite edges of each ceiling. Avoid use of less-than-half width units at borders, and comply with reflected ceiling plans wherever possible.

- Symmetrically locate grid layout in each space. Coordinate work with other trades so that lighting fixtures, grilles, and other ceiling fixtures work with grid layout.

- Do not use universal splices or other splices which would obstruct passage of recessed lighting fixtures through grid openings or limit fixture relocation upon flanges of ceiling grids.

- Support suspension system from structure above, not from ductwork, metal deck, equipment or piping.

- Space hangers not more than 6 inches from ends and not more than 4 feet on center.

- Install edge moldings at the perimeter of each ceiling area and at locations where edge of units would otherwise be exposed.

  - Secure moldings to building construction by fastening with screw anchors into substrate through holes drilled in vertical leg. Space holes no more than 3 inches from each end and not more than 16 inches on center along each molding.

  - Level moldings with ceiling suspension system, to a level tolerance of 1/8 inch in 12 feet.

  - Miter corners of moldings accurately to provide hairline joints, securely connected to prevent dislocation. Cope exposed flanges of intersecting suspension system members, so that flange faces are flush.

  - Furnish additional tees for supporting grilles, diffusers and lighting fixtures. Refer to reflected ceiling, HVAC and electrical plans for locations.

  - Provide tegular edge at walls and at other abutting vertical surfaces. Field paint cut edges to surface color and sheen.

- Arrange units and orient directionally-patterned units, if any, in manner shown on reflected ceiling plans.

3.03 Cleaning

- Clean exposed surfaces of ceilings, trim, edge moldings and suspension members to comply with manufacturer's instructions for cleaning and touch-up of minor finish damage.

- Remove work which cannot be successfully cleaned and repaired to permanently eliminate evidence of damage.

3.04 Protection

- Provide required protection for the ceilings, including dust control, so that the work will be without damage and deterioration at the time of acceptance by the Owner.