Suggested Specification Guidelines for Planium Floor System

Specifying Gage Flooring is a simple process. Follow the guidelines listed below. Complete architectural (Technical) specifications and installation guidelines can be downloaded from our website at www.gagecorp.net or contact the factory.

Item:		Steel Floor System by Planium

Design:	  Armor     Black Organic

System:	Rubber support system

Metal:		304 SS face, galvanized core (Armor)

Heat treated steel (Black Organic)

Size:		23.6” x 23.6” (60 cm x 60 cm), tile dimensions

Reveal:	0.27” (0.7 cm)

Weight:	22 lbs. (10 kg) for each tile and rubber underlayment

Thickness:	0.27” (0.7 cm)